| Device | Application | Input Voltage | Output Voltage & Current | Output Power |
| --- | --- | --- | --- | --- |
| NCP1342 | Industry | 90Vac - 264Vac | 65W / 9V / 7A | 65W |
| Efficiency | Standby Power | Vout Ripple | Board Size | Protection |
| 90.83% | 0.38mW | 120mVp-p | 100mmX50mX30mm | OVP / OCP / OTP |

| Efficiency | TEST CONDITION |
| --- | --- |
|  |  | Input Voltage : 230 VAC Output : Full Load |
|  | 100% 75% 50% 25% Standby Power Vout（V） 9.213 9.271 9.322 9.351 0.38W Iout （A） 7.057 5.232 3.492 1.748 Pin （W） 71.582 53.568 36.297 18.535 EFF 90.83% 90.55% 89.68% 88.19% |

# Protection Function Test

| NO | TEST ITEM | SPECIFICATION | TEST CONDITION | RESULT |
| --- | --- | --- | --- | --- |
| 1 | Over Voltage Protection | Output Voltage：10.8V~13.5V | Input Voltage: 230VAC | 12.2V OVP occur at 230Vac condition |
| 2 | Over Current Protection | CH1: 7.7A~ 10.5A | Input Voltage: 230VAC | 9.15A enter over current mode auto recovery mode At input 230Vac |
| 3. | Output Short Protection | Shout output 1 hour No Damage | Input Voltage: 230VAC | NO DAMAGE |

# Component temperature Test

| Test conditon: Input Voltage 100Vac@Full Load burn-in 2Hours |
| --- |
| Device Temperature | Mosfet | Transformer | Maine IC | Ta |
|  | 95.4℃ | 97.7℃ | 86.5℃ | 42.5℃ |

# Power Mosfet Stress

| TEST Item | Test Condition |
| --- | --- |
| Power mosfet Vds stress normal state | Input Voltage : 264Vac Output : Full Load |
| Dynamic Test | Input Voltage：230Vac Output：Full Load 4.16ms/Min Load 4.16ms |
|  | Ripple Noise | Input Voltage: 230Vac Output：Full Load |

# E.M.C TEST

| TEST Item | Test Condition |
| --- | --- |
| Conduction | Input Voltage : 230Vac50Hz Output : Full Load |
| Radiation | Input Voltage : 230Vac50Hz Output : Full Load |
|  | E.S.D | EN61000-4-2 AIR：8KV / Contact：4KV | Input ： 230 Vac/50Hz Output：Full Load |  |
|  | E.F.T | EN61000-4-4 2KV | Input ：230Vac/50Hz Output：Full Load |  |
|  | SURGE | IEC61000-4-5 L-N ：1KV L,N-：2KV | Input ： 230 Vac/50Hz Output：Full Load Ta：25℃ |  |